|  | Assignment No. 1 SEMESTER SPRING 2011 CS501-Advance Computer Architecture | Total Marks: 20 Due Date: 18/04/2011 |
| --- | --- | --- |
| Instructions Please read the following instructions carefully before submitting assignment: It should be clear that your assignment will not get any credit if: The assignment is submitted after due date. The submitted assignment does not open or file corrupt. The assignment is copied. There is not mentioned the student Id in the assignment or name of file is other than student ID GOOD LUCK |
| Question No: 1 | Marks: 4+4+4+4=16 |
| Consider the following equation Z= (a-b)-16(c+d) You have to solve this equation using the following Three Address instruction Two Address instruction 1 Address Instruction 0 Address Instruction Solution: 3 address instruction 2 address instruction 1 address instruction 0 address instruction Sub x,a,b Add r,c,d Mul s,r,16 Sub z,x,s Load y,a Sub y,b Load s,c Add s,d Mul s,16 Sub y,s Store z,y Lda c Adda d Mula 16 Sta s Lda a Suba b Suba s Sta z push c push d add push 16 mul push a push b sub sub popz |
| Question No: 2 Marks: 2+ 2= 4 |
| A digital computer has a common bus system for 16 registers of 32 bit each. The bus is constructed with multiplexers. Then answer the following questions How many selection inputs are there in each multiplexer? 16 registers = 24 => 4 selection inputs What sizes of multiplexers are needed? 16 registers => 16 x 1 line multiplexers are needed |