ASSIGNMENT # 2(Solution)

CS501

Q.1

Specify the condition for the branch instruction and the status of the PC after the branch instruction executes with a true branch condition.

Solution:

| Instruction | Condition | PC status |
| --- | --- | --- |
| Jump[20] | Always | PC← PC+20 |
| Jnz r3,[33] | If R[3] ≠ 0 | PC← PC+33 |
| Jz r1,[16] | If R[1] = = 0 | PC← PC+16 |
| Jpl r5,[37] | If R[5] ≥0 | PC← PC+37 |
| Jmi r7,[40] | If R[7] < 0 | PC← PC+40 |

Q.2

Identify the addressing modes and Register Transfer Language (RTL) description (meaning) for the given Falcon-A instructions

Solution:

| Instruction | Addressing Mode | RTL description(meaning) |
| --- | --- | --- |
| Load r3,[r5+27] | Displacement | R[3] ← M[R[5] +27] |
| Jnz r5,[15] | Relative | (If R[5] ≠ 0): PC← PC+15 |
| Shiftl r3,r2,5 | Immediate | Shift r2 left 5 times and store in r3 |
| Add r6,r5,r7 | Register | R[6] ← R[5] + R[7] |
| Subi r4,r3,17 | Immediate | R[4] ← R[3] -17 |