CS 610 Computer Networks

Assignment # 03 Solution

Spring 2011

Total Marks = 20

Deadline

Your assignment must be uploaded / submitted before or on June 7, 2011

Upload Instructions

Please view the assignment submission process document provided to you by the

Virtual University.

Rules for Marking

Please note that your assignment will not be graded if:

• It is submitted after due date

• The file you uploaded does not open

• The file you uploaded is copied from someone else or from internet

• It is in some format other than .doc

Objective

The assignment has been designed to develop the understanding about the concept of Classless and Classful IP addressing.

Note: Material that is an exact copy from handouts or internet would be graded

zero marks. Your solution should consist of the material found through different sources and written in your own words.

Assignment Statements:

Q1: Star organization is using five classless and classful IP addresses in its network. Network engineer wants to compute all the entries which are given in the table. Please fill all entries and mention which methods are used for computing all these entries. (Write only the names of methods). In last row proper steps are required for binary conversion.

| Address | 9.1.4.5/16 | 145.24.102.1/24 | 201.16.1.100/24 | 137.41.102.1/22 | 193.11.11.100/27 | 9.1.4.5/16 | Methods |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Mask | 255.255.0.0 | 255.255.255.0 | 255.255.255.0 | 255.255.252.0 | 255.255.255.224 | 255.255.0.0 | Default mask according to class range and it is changed according to subnet bits. |
| Number of Network Bits | 8 | 16 | 24 | 16 | 24 | 8 | According to class range |
| Number of Host Bits | 16 | 8 | 8 | 10 | 5 | 16 | Class range according to subnet bit |
| Number of Subnet Bits | 8 | 8 | 0 | 6 | 3 | 8 | Borrow host bits for networks |
| Number of Hosts Per Subnet | 216 – 2, or 65,534 | 28 – 2, or 254 | 28 – 2, or 254 | 210 – 2, or 1022 | 25 – 2, or 30 | 216 – 2, or 65,534 | 2n-2 (n represents no. of host bits) |
| Class of address | A | B | C | B | C | A | By ranges -A 128-191-B 192-223 -C |
| Change address into binary notation | 00001001 00000001 00000100 00000101 | 10010001 00011000 01100110 00000001 | 11001001 00010000 00000001 00110100 | 10001001 00101001 00110110 00000001 | 11000001 00001011 00001011 00110100 | 00001001 00000001 00000100 00000101 | L.CM or by Decimal notation |